DTMF Decoder Project Report
google doc
https://onedrive.live.com/edit.aspx?cid=70e0eade33dc645f&id=documents&resid=70E0EADE33DC645F!3630&app=Word&&wdPid=b8d2513
Contents

# Introduction

# DTMF stands for Dual Tone Multi Frequency. This is an in-band telecommunication signaling system using voice-frequency band over telephone lines between telephone equipment and other communications devices and switching centers. DTMF was first developed in the Bell System in the USA, and became known under the trademark Touch-Tone for use in the pushbutton telephones supplied to telephone customers, starting in 1963.[1] DTMF replaced the clockwork dial made of moving parts which was getting more and more impractical to use as the number of telephone users increased exponentially.
# DTMF is used to represent up to 16 keys (most telephones only use 12 of these). Each key is represented by two differenct frequencies. The first bin (lower frequencies) consits of frequencies under 1kHz and the second bin (Upper bin) consists of frequencies above 1.2kHz. The combination of the two tones will be distinctive and different from tones of other keys and these tones cannot be mimicked by voice or random signals [2]. The DTMF Frequencies are shown in the figure below:
Illustration 1: Picture showing the DTMF Frequencies used to represent each key.
# DTMF detection is used to detect DTMF signals in the presence of speech and dialing tones pulses. Other applications of DTMF include, but not limited to, computer applications such as voice and electronic mail, call forwarding [3], controlling robots, automated locking and unlocking systems, displaying dialed numbers on a screen and sharing information consisting of numbers across various network sytems.[2]
# The intent of this project is to design a DTMF Decoder and implement it in Java. I decided to choose this project because it dives into important concepts in both “sides” of my degree, that is Signal Processing and Software Design.
# Research and Background
Although I did a introductory course to Signals and Systems in first semester of my second year, there was still a lot of concepts I had not grasped yet. Most of the knowledge needed to tackle this project was only going to be covered in my third year courses therefore after a long talk with my mentor who shed some much needed light on the project, I spent the whole first week researching on signal processing techniques by reading articles [4] and lectures on MIT OpenCourseWare [5]. All these helped build my understanding of signal processing and detection.
## Fast Fourier Transform
This is a DFT algorithm(s) which can compute the DFT of a sequence in less computations for the same number of sample points. Cooley and Turkey and usually credited for inventing the algorithm in 1965 although the development of of fast algorithms of FFTs can be traced back to Gauss's unpublished work in 1805. [8]
A possible path to take could be using the FFT to get the whole frequency spectrum. This is definitely a cumbersome computation but it will allow me to detect other frequencies in the signal and decide where certain signals should be rejected or not.
After looking at previous similar projects, most of which were implemented in Assembly and C for micro-controller projects, I noticed most of them used the Goertzel Algorithm to detect the DTMF frequencies. I decided to do more research on reasons why and it turns out it is a much faster method for computing DFTs (Direct Fourier Transform) for specific frequencies.
## Goertzel's Algorithm
Created by Gerald Goertzel in 1958, the Goertzel Algorithm is a Digital Signal Processing technique that is used to efficiently compute individual terms of a Direct Fourier Transform (DFT). It returns the real and imaginary frequency components that a regular DFT or Fast Fourier Transform (FFT) would.
Like the DFT, the Goertzel algorithm analyses one selectable frequency component from a discrete signal.[6][7] Unlike direct DFT calculations, the Goertzel algorithm applies a single real-valued coefficient at each iteration, using real-valued arithmetic for real-valued input sequences. For covering a full spectrum, the Goertzel algorithm has a higher order of complexity than (FFT) algorithms; but for computing a small number of selected frequency components, it is more numerically efficient.
The Goertzel Algorithm may be used to directly obtain DFT data about the 8 DTMF frequencies and compare their magnitudes to determine which tone is being represented.
# Software Implementation
After the research I was advised to start by protoyping the solution in MatLab before implementing it in Java. MatLab is a high-performance language for technical computing. It integrates computation, visualization, and programming in an easy-to-use environment where problems and solutions are expressed in familiar mathematical notation. [9] Because I was new to signal processing, it was important for me to use a tool like MatLab to visualise the data and focus on developing the algorithms instead of spending a lot of time trying to code functions which I had easy access to in MatLab.
## Test Data
The first step was to generate test data that I would use to test the decoder. My mentor gave me a guideline of how a good DTMF decoder should perform and told me to look up ITU-T recommendations on DTMF tones. The decoder had to meet the ITU Recommendation as stated in ITU-I Recommendation Q.23 [10] and ITU-I Recommendation Q.24 [11]. Each administration has it's own specifications but most of them overlap each other. A summary of the recommendations is shown below (taken from ITU-T Q.24 [11]) :
Signal Frequencies:
- Low Band (Hz): 697, 770, 852, 941
- High Band (Hz): 1209, 1336, 1477, 1633
Frequency Tolerances:
- Max. accepted frequency offset: <=1.5% to 1.8% (depending on Administration)
- Min. rejected frequency offset: >= 3.5% to 7.5% (depending on Administration)
Power Levels per Frequency:
- Power range: -27dBm to 0dBm
- Maximum twist (Power difference between the two frequencies): 5 to 10 dBm (depends on Administration)
Signal Timing:
- Min. accepted tone duration: 40ms
- Min. pause (silence between tones): 30ms to 70ms (depending on Administration)
- Max. rejected tone duration: 20ms
- Max. signal interruption: 10ms

I had to generate Test Data to test all the conditions above. My Test Data was generated as follows:
- The sequence of tones will be randomly determined (choosing from the 16 available DTMF characters) and the length of the sequence will also vary randomly from 5 tones to 50 tones per file.
- The duration of each DTMF tone will be varied randomly between 40ms and 100ms.
- The duration of the pause between DTMF tones will be randomly varied between 30ms and 100ms.
- To vary the power of the signal between 0dBm and -27dBm, the amplitude of the signal will be varied from 0.045 (-27dBm) to 1.0 (0dBm).
Random duration of pauses and tones will ensure that the frames used in the decoding process do not have the same alignment.
## Prototyping
This was done in MatLab. I decided to use the Goertzel's Algorithm approach because of it's performance advantages over the FFT. After some brain storming with my mentor, I came up with the following outline of the decoder:
- The array of samples will be split into short frames (each frame will be a short period of about 40ms but this duration will be optimized later). Because the Goertzel Algorithm's performance did not depend on a specific bin size (as with the FFT where the bin size has to be a power of 2), I could vary the bin size to make the decoder more accurate. The frames overlap each other by 50% which means more frames are processed, hence decreasing performance, but this will make sure the frames cover the shortest tones properly. The longer these frames were, the better the resolution will be in the frequency spectrum but the poorer it would be in the time domain. An example of how the samples will be divided is shown below.

  Illustration 2: An example of how the samples may be split to create frames which can be processed separately.
- The frames will each be transformed using the Goertzel Algorithm to obtain the magnitudes of the 8 DTMF frequencies in the frame. One of the ITU-T recommendations is that the frequencies can have an offset of up to 1.5%. This offset could be accounted for by using 3 or 4 frequncies for each DTMF frequency when transforming the frames and then summing up these 2 or 3 magnitudes. So instead of passing 8 frequencies into the Goertzel Algorithm, I used about 25 different frequencies. The two illustrations below show how the plots of the magnitudes from a frame in the “tone” region and in the “pause” region:

Illustration 3: Plot of the DFT Magnitudes of the 8 DTMF frequencies for a frame in the "tone" region. This particular tone represents a "1".
Illustration 4: Plot of the DFT Magnitudes of the 8 DTMF frequencies for a frame in the "pause" region.
- After trasnforming the frames, I used the DFT data to distinguish between frames in the “tone” region and frames in the “pause” region. From the pictures above, it can be seen that the average of the magnitudes for the “tone” region are much larger than those in the “pause” region. To distinguish the “pause” frames from the “tone” ones, I decided that the “silent” frames will be those with a mean DFT magnitude less than 70% of the average of the top 3 frames. An illustration of this is shown below:
- After filtering out the frames with the tones, I pass the data into a function which will determine the character represented by the frame by looking at the frequencies present in the frame.
After implementing this algorithm in Matlab I ran the decoder on test data and after tweaks and changed, the decoder had a success rate of 98% on 40,000 test files. A success is recorded when the whole sequence has been successfully and accurately decoded. Instead
## Java Implementation

## Testing

## API Specifications

# Possible Improvements

# Conclusion

# References

### 1) DODD, A. Z. The essential guide to telecommunications
2) (picture) http://www.engineersgarage.com/tutorials/dtmf-dual-tone-multiple-frequency
3) G. L. Smith, Dual-Tone Multifrequency Receiver Using the WE DSP16 Digital Signal
Processor, AT&T Application Note.
4)
2010 4th International Symposium on Communications, Control and Signal Processing (ISCCSP 2010) p1-5

5) Alan Oppenheim. 6.341 Discrete-Time Signal Processing, Fall 2005. (Massachusetts Institute of Technology: MIT OpenCourseWare), http://ocw.mit.edu (Accessed 26 Jan, 2016). License: Creative Commons BY-NC-SA
6) Mock, P. (March 21, 1985), "Add DTMF Generation and Decoding to DSP-μP Designs" (PDF), EDN, ISSN 0012-7515; also found in DSP Applications with the TMS320 Family, Vol. 1, Texas Instruments, 1989.
7) Chen, Chiouguey J. (June 1996), Modified Goertzel Algorithm in DTMF Detection Using the TMS320C80 DSP (PDF), Application Report, SPRA066, Texas Instruments
8) Heideman, Michael T.; Johnson, Don H.; Burrus, C. Sidney (1985-09-01). "Gauss and the history of the fast Fourier transform". Archive for History of Exact Sciences 34 (3): 265–277. doi:10.1007/BF00348431. ISSN 0003-9519.
9) http://cimss.ssec.wisc.edu/wxwise/class/aos340/spr00/whatismatlab.htm
10) itu-t q23
11) itu-t q24