DTMF Decoder

Define DTMF, history behind it and explain how it works

Applications of DTMF

prototyping

test data

testing in prototyping phase

java implementation

testing java program

possible improvements

conclusion

## Introduction
This is a project to develop a JAVA program to implement a DTMF decoder.

DTMF stands for Dual Tone Multi Frequency. This is an in-band telecommunication signaling system using voice-frequency band over telephone lines between telephone equipment and other communications devices and switching centers. DTMF was first developed in the Bell System in the USA, and became known under the trademark Touch-Tone for use in the pushbutton telephones supplied to telephone customers, starting in 1963.[1] DTMF replaced the clockwork dial made of moving parts which was getting more and more impractical to use as the number of telephone users increased exponentially.

### How DTMF works [2]
DTMF uses a 12 or 16 button keypad. Each key generates two tones of different frequencies; one from DTMF High Frequency group and the other from DTMF Low Frequency group. The combination of the two tones will be distinctive and different from tones of other keys and these tones cannot be mimicked by voice or random signals. The DTMF Frequencies are shown in the figure below:

Figure 1: Diagram showing the DTMF Low and High Frequencies for each key on a telephone keypad.[2]

Other applications of DTMF include, but not limited to, controlling robots, automated locking and unlocking systems, displaying dialed numbers on a screen, share information consisting of numbers across various network sytems, etc...
### Prototyping

First step was to create sample test tones in Audacity with a bit rate of 8kHz. These will be pure DTMF tones, each tone will be approximately 160ms with silences of 96ms.
Because I knew the exact frequencies I was looking for, I used Goertzel’s Algorithm to extract a frequency spectrum of the frames showing just the DTMF frequencies. A short insight into Goertzel’s Algorithm.
### Goertzel’s Algorithm

Created by Gerald Goertzel in 1958, the Goertzel Algortihm is a Digital Signal Processing technique that is used to efficiently compute individual terms of a Direct Fourier Transform (DFT). It returns the real and imaginary frequency components that a regular DFT or Fast Fourier Transform (FFT) would.
Like the DFT, the Goertzel algorithm analyses one selectable frequency component from a discrete signal.[6][7][8] Unlike direct DFT calculations, the Goertzel algorithm applies a single real-valued coefficient at each iteration, using real-valued arithmetic for real-valued input sequences. For covering a full spectrum, the Goertzel algorithm has a higher order of complexity than (FFT) algorithms; but for computing a small number of selected frequency components, it is more numerically efficient.

I have not included most of the theory behind the algorithm because it is beyond my scope (for now) but I have tried to outline how I used it in the project. The following is mostly obtained from www.embedded.com [5] which has a simplified outline of the algorithm.
Just like the FFT, the algorithm works with blocks of sample points. For each frequency to be calculated, the following are needed:
- the sampling frequency (Fs).
- block size (N) i.e number of samples being used.
- Precomputed one sine and one cosine term. (s and c)
- Precomputed coefficient (coeff)
The usual Nyquist Rules apply which means that Fs will have to be at least twice that of the highest frequency in question. The frequency of interest has to be an integer factor of the sampling frequency.
N has the same properties as that of the block size in a regular FFT. N controls the frequency resolution in the frequency spectrum of the signal which is given as Fs/N. N can be chosen such that the frequency resolution covers enough of the DTMF frequencies within their tolerances but it must also be small enough to cover the minimum tone duration. One of the biggest advantages of the Goertzel Algorithm is that unlike the FFT, N does not have to be a power of 2 for it to work efficiently.
After Fs and N are determined and with target as the target frequency, the following calculations are made;
c = cos(w)
s = sin(w)
coeff = 2 * c
k = (int)(0.5 x N x target x 1/Fs)
w = (2*π/N)*k
Three variables will be needed to continue, these will be Q0, Q1 and Q2.
Q1 and Q2 are initialised to zero at the beginning of each block of samples then for each sample:
Q0 = coeff * Q1 - Q2 + sample
Q2 = Q1
Q1 = Q0

After running this per sample, the real and imaginary frequency components are given by:
real = (Q1 - Q2 * c)
imag = (Q2 * s)
magnitude2 = real2 + imag2

Next I had to determine the size of the frames that will be used for decoding the data. After research and advice from Albert, for the Fast Fourier Transform to work fast, the frame sizes should have 2n samples. Because of this restriction, the frame length range from 22ms to 45ms. For popular sample rates, the frames sizes are as follows:
Sample Rate (Hz)	Frame size used in program
8000	32ms (256 samples)
11 025	23ms (256 samples)
16 000	32ms (512 samples)
22 050	23ms (512 samples)
32 000	32ms (1024 samples)
44 100	23ms (1024 samples)
48 000	43ms (2048 samples)
96 000	43ms (4096 samples)
176 400	23ms (4096 samples)
192 000	43ms (8192 samples)
352 800	23ms (8192 samples)

Figure 2: Table showing the frame sizes used for corresponding sampling rates.

After splitting the data into short frames, each of these frames will be filtered using the Goertzel function in MatLab. I created a function which returned an array DFT data of the DTMF frequencies in each of the frames. A plot of these arrays is shown below:

Figure 3: Plot of the DFT Magnitudes of a frame in the "tone" region

Figure 4: : Plot of the DFT Magnitudes of a frame in the "silent" region
NB: observe that the magnitudes of the frequencies in the “silent” region were much smaller and had random values compared to those in the “tone” region.
Next task was to find a way to distinguish between “tone” and “silent” regions and then retrieve the tone represented by the frames that weren’t “silent” ones. There is no formal way of doing this so had to think of heuristic methods. After some observation, noticed that the average magnitudes of frames that were from the “tone” region were much greater than the average of the frames in the “silent” region. This is illustrated in the graph below:
To distinguish “silent” frames from “tone” frames, I decided that “silent” frames will be the frames with mean less than 10% of the average of the top 3 frames in the first 20 frames of the data. An illustration of this is shown below;

The peaks in the Figure above show presence of a tone. Frames with a mean below the dotted red line will be “silent” tones.

Detection Efficiency
After the design of the first prototype, the filter had to be improved to meet the ITU Recommendation as stated in ITU-I Recommendation Q.23 [3] and ITU-I Recommendation Q.24 [4]. Each administration has it's own specifications but most of them overlap each other. A summary of the recommendations is shown below (taken from ITU-T Q.24 [4]) :
Signal Frequencies:
- Low Band (Hz): 697, 770, 852, 941
- High Band (Hz): 1209, 1336, 1477, 1633
Frequency Tolerances:
- Max. accepted frequency offset: <=1.5% to 1.8% (depending on Administration)
- Min. rejected frequency offset: >= 3.5% to 7.5% (depending on Administration)
Power Levels per Frequency:
- Power range: -27dBm to 0dBm
- Maximum twist (Power difference between the two frequencies): 5 to 10 dBm (depends on Administration)
Signal Timing:
- Min. accepted tone duration: 40ms
- Min. pause (silence between tones): 30ms to 70ms (depending on Administration)
- Max. rejected tone duration: 20ms
- Max. signal interruption: 10ms

I had to generate Test Data to test all the conditions above. My Test Data was generated as follows:
- The sequence of tones will be randomly determined (choosing from the 16 available DTMF characters) and the length of the sequence will also vary randomly from 5 tones to 50 tones per file.
- The duration of each DTMF tone will be varied randomly between 40ms and 100ms.
- The duration of the pause between DTMF tones will be randomly varied between 30ms and 100ms.
- To vary the power of the signal between 0dBm and -27dBm, the amplitude of the signal will be varied from 0.045 (-27dBm) to 1.0 (0dBm).
- To random duration of pauses and tones will ensure that the frames used in the decoding process do not have the same alignment.

Changes made to the filter during/after testing (MatLab)
I ran tests decoding 40,000 test files that were generated using the specifications on the previous page. The success rate was 98%.

- The original frame size of 256 gave a success rate of only 89%. This is because of the frequency tolerance recommended by the ITU-T which meant that my decoder had to be more precise in the Frequency Domain. This came at a cost of less accuracy in the Time Domain though since the frame size was increased but this was dealt with in the next change described below. After some research I found out that the Goertzel Algorithm's performance is not affected by the size of the frame (I.e it does not have to be a power of 2). The new frames size is 370 which was worked out by testing several different frame sizes from 200 up to 400.
- The frames now overlap by 50% which effectively doubles the number of frames used in the decoding process. This offsets the effect of increasing the frame size described above. Precision in the time domain is still very important because, at a sampling frequency of 8kHz, each frame is now 64ms long which is longer than the minimum accepted tone length of 40ms and this affects the accuracy of the decoder in the Time Domain.
- Instead of checking for one specific DTMF frequency when using the Goertzel algorithm, I changed the decoder such that it check the range of frequencies within the maximum allowed tolerance of 1.5%. This unfortunately has a negative impact of performance because 274 frequencies are now being transformed by the Goertzel Algorithm instead of just 8. Nevertheless, the algorithm is still much faster than using FFT.

## Java Implementation

Implementing the matlab code in java was a challenge because Java does not have libraries with most of the functions I used in MatLab. After some consultation with my Mentor Albert, I realised that my algorithm was slow and used up a lot of RAM because I was loading the whole .wav file before decoding. This would be a problem when decoding thousands of files in parallel. The PC would quickly run out of memory. To combat this I had to use an input stream and process the wav files frame-by-frame instead of loading the whole file. This proved to be much faster and also more efficient in terms of resource usage.
The basic algorithm goes like this:
- open an input stream for the .wav file.
- Determine the bin size (frameSize in my program) for the Goertzel Algorithm using the sampling frequency. For my decoder, the frameSize is 44.5ms long.
- NB: After some more testing in Java, I decided to have the frames overlap by 33% instead of 50%.
- Read a frame from the .wav file and first calculate the signal's power. If the power is too low for detection the frame will be rejected and treated as a pause.
- If the signal strength in the fram is strong enough, the frame is transformed using Goertzel's Algorithm using 3 to 4 different frequencies within the bin of toleraces of the DTMF frequencies. The function that transforms the frame returns an array with 8 figures representing the powers of each DTMF Frequency in the frame.
- After transforming the frame, it is checked for noise. If any noise exists, the frequency spectrum of the signal will have peaks located at random positions. If the frame contains a DTMF tone, the peak for that frequency should still stand out depending on the Signal-To-Noise Ratio (SNR) of the signal.
  Human speech and other random tones also had to be detected and filtered out. To achieve this, the ratio of the two highest peaks (each from the higher and lower DTMF frenqueny bins) to the sum of all the magnitudes was calculated and compared to a predetermined value. The higher this ratio is, the lower the SNR is. If the frame is too noisy, it is rejected and treated as a pause.
- After checking for noise, the two peaks from each bin are identified and then used to determine with DTMF character is being represented.
- After retrieving the character being represented by the frame, it is kept in a temporary variable for later usage.
- If two, three or four consecutive frames decode to give the same DTMF character, this will be recorded as a hit. The number of consecutive characters used to determine this depend on the minimum tone duration. For a minimum duration of 40ms, there must be at least two consecutive characters. For a minimum duration of 60ms, the must be at least 3 consecutive characters and so on. Using a longer or shorter minimum tone duration has advantages and disadvantages. If a shorter duration is used it means that the decoder follows ITU-T Recommendations better and shorter tones can be detectced. The down side is that the hit-rate is poor when decoding voice recordings or other recordings with a lot of background noise. If a longer minimum tone duration is used, the decoder will no longer follow ITU-T standards but the hit rate improves greately when decoding voice recordings or audio with a lot of background noise.
- This whole process continues untill there are no more samples left in the file.
### Noise and Speech

MatLab has a funtion called “Add White Gaussian Noise” { awgn(x,snr) } which allows the user to add white gaussian noise to a signal, x, to produce another signal with a SNR given specified by the user. I used this funtion to produce data with varying SNR from 5dB to 50dB. Besides the added noise, the data used was the same as that used in previous tests and made using the same test variables. I ran my decoder of these files and obtained the following results.
[[graph of SNR vs success rate]]
From the tests it is evident that the decoder can handle signals with a SNR of XxdB. The decoder's noise filter also had to be adjusted to reject speech and other random tones which proved to be a problem but thanks to the way the DTMF frequencies were chosen, it is rare for a random signal (or speech) to have peaks in both the higher and lower frequency bands. I used this assumption to improve the filter and it worked much better.

References

### 1) DODD, A. Z. The essential guide to telecommunications
2) (picture) http://www.engineersgarage.com/tutorials/dtmf-dual-tone-multiple-frequency
3) (pdf ITU q23) https://www.itu.int/rec/dologin_pub.asp?lang=e&id=T-REC-Q.23-198811-I!!PDF-E&type=items
4) (pdf itu q24) https://www.itu.int/rec/dologin_pub.asp?lang=e&id=T-REC-Q.24-198811-I!!PDF-E&type=items
5) http://www.embedded.com/design/configurable-systems/4024443/The-Goertzel-Algorithm
6) Mock, P. (March 21, 1985), "Add DTMF Generation and Decoding to DSP-μP Designs" (PDF), EDN, ISSN 0012-7515; also found in DSP Applications with the TMS320 Family, Vol. 1, Texas Instruments, 1989.
8) Chen, Chiouguey J. (June 1996), Modified Goertzel Algorithm in DTMF Detection Using the TMS320C80 DSP (PDF), Application Report, SPRA066, Texas Instruments
9) Schmer, Gunter (May 2000), DTMF Tone Generation and Detection: An Implementation Using the TMS320C54x (PDF), Application Report, SPRA096a, Texas Instruments