DTMF Decoder

Define DTMF, history behind it and explain how it works

Applications of DTMF

prototyping

testing in prototyping phase

java implementation

testing java program

possible improvements

conclusion

## Introduction
This is a project to develop a JAVA program to implement a DTMF decoder.

DTMF stands for Dual Tone Multi Frequency. This is an in-band telecommunication signaling system using voice-frequency band over telephone lines between telephone equipment and other communications devices and switching centers. DTMF was first developed in the Bell System in the USA, and became known under the trademark Touch-Tone for use in the pushbutton telephones supplied to telephone customers, starting in 1963.[1] DTMF replaced the clockwork dial made of moving parts which was getting more and more impractical to use as the number of telephone users increased exponentially.

### How DTMF works [2]
DTMF uses a 12 or 16 button keypad. Each key generates two tones of different frequencies; one from DTMF High Frequency group and the other from DTMF Low Frequency group. The combination of the two tones will be distinctive and different from tones of other keys and these tones cannot be mimicked by voice or random signals. The DTMF Frequencies are shown in the figure below:

Figure 1: Diagram showing the DTMF Low and High Frequencies for each key on a telephone keypad.[2]

### Applications of DTMF

// TODO
### Prototyping

First step was to create sample test tones in Audacity with a bit rate of 8kHz. These will be pure DTMF tones, each tone will be approximately 160ms with silences of 96ms.
Because I knew the exact frequencies I was looking for, I used Goertzel’s Algorithm to extract a frequency spectrum of the frames showing just the DTMF frequencies. A short insight into Goertzel’s Algorithm.
// TODO
Next I had to determine the size of the frames that will be used for decoding the data. After research and advice from Albert, for the Fast Fourier Transform to work fast, the frame sizes should have 2n samples. Because of this restriction, the frame length range from 22ms to 45ms. For popular sample rates, the frames sizes are as follows:
Sample Rate (Hz)	Frame size used in program
8000	32ms (256 samples)
11 025	23ms (256 samples)
16 000	32ms (512 samples)
22 050	23ms (512 samples)
32 000	32ms (1024 samples)
44 100	23ms (1024 samples)
48 000	43ms (2048 samples)
96 000	43ms (4096 samples)
176 400	23ms (4096 samples)
192 000	43ms (8192 samples)
352 800	23ms (8192 samples)

Figure 2: Table showing the frame sizes used for corresponding sampling rates.

After splitting the data into short frames, each of these frames will be filtered using the Goertzel function in MatLab. I created a function which returned an array DFT data of the DTMF frequencies in each of the frames. A plot of these arrays is shown below:

Figure 3: Plot of the DFT Magnitudes of a fram in the "tone" region

Figure 4: : Plot of the DFT Magnitudes of a fram in the "silent" region
NB: observe that the magnitudes of the frequencies in the “silent” region were much smaller and had random values compared to those in the “tone” region.
Next task was to find a way to distinguish between “tone” and “silent” regions and then retrieve the tone represented by the frames that weren’t “silent” ones. There is no formal way of doing this so had to think of heuristic methods. After some observation, noticed that the average magnitudes of frames that were from the “tone” region were much greater than the average of the frames in the “silent” region. This is illustrated in the graph below:
To distinguish “silent” frames from “tone” frames, I decided that “silent” frames will be the frames with mean less than 10% of the average of the top 3 frames in the first 20 frames of the data. An illustration of this is shown below;

The peaks in the Figure above show presence of a tone. Frames with a mean below the dotted red line will be “silent” tones.
References

### 1) DODD, A. Z. The essential guide to telecommunications
2) (picture) http://www.engineersgarage.com/tutorials/dtmf-dual-tone-multiple-frequency